## Slide 1: QuickRelease: A Throughput-oriented Approach to Release Consistency on GPUs
Blake A. Hechtman†§, Shuai Che†, Derek R. Hower†, Yingying Tian†Ϯ,
Bradford M. Beckmann†, Mark D. Hill‡†, Steven K. Reinhardt†, David A. Wood‡†
§Duke University
ϮTexas A&M University
‡University of Wisconsin-Madison
†Advanced Micro Devices, Inc.

## Slide 2: Executive summary
GPU memory systems are designed for high throughput
  Goal: Expand the relevance of GPU compute
  Requires good performance on a broader set of applications
  Includes irregular and synchronized data accesses
Naïve solution: CPU-like cache coherent memory system for GPUs
  Efficiently supports irregular and synchronized data accesses
  Costs significant graphics and streaming performance → unacceptable
QuickRelease
  Supports both fine-grain synchronization and streaming applications
  Enhances current GPU memory systems with a simple write tracking FIFO
  Avoids expensive cache flushes on synchronization events

## Slide 3: OUTLINE
Motivation
  Current GPUs
  Future GPUs
Memory System Design & Supporting Synchronization
  Write-through with cache flushes (WT)
  CPU-like “Read-for-Ownership” cache coherence (RfO)
QuickRelease
Results
Conclusions / Future work
Notes: Consider removing this slide.

## Slide 4: Current gpuS
Maintain Streaming and Graphics performance
  High bandwidth, latency tolerant L1 and L2 caches
  Writes coalesced at the CU and write-through
CPU0
L1
L2
CPU1
L1
L2
CU1
L1
CU0
L1
LLC
Directory / Memory
CPU
GPU
Notes: Maintaining coherence with the CPU requires coalescing writes with the CPU.
Describe FIGURE

## Slide 5: Future GPUs
Expand the scope of GPU compute applications
  Support more irregular workloads efficiently
  Support synchronized data efficiently
  Leverage more locality
Reduce programmer effort
  Support over-synchronization efficiently
  No labeling volatile (rw-shared) data structures
Allow more sharing than OpenCL 1.x (e.g. HSA or OpenCL 2.0)
  Global synchronization between workgroups
  Heterogeneous kernels with concurrent CPU execution w/ sharing

## Slide 6: How can we support both?
To expand the utility of GPUs beyond graphics, support:
  Irregular parallel applications
  Fine-grain synchronization
  Both will benefit from coherent caches
But traditional CPU coherence is inappropriate for:
  Regular streaming workloads
  Coarse-grain synchronization
Graphics will still be a primary application for GPUs
Thus, we want coherence guided by synchronization
  Avoid the scalability challenges of “read for ownership” (RFO) coherence
  Maintain streaming performance with coarse-grain synchronization

## Slide 7: OUTLINE
Motivation
  Current GPUs
  Future GPUs
Memory System Design & Supporting Synchronization
  Write-through with cache flushes (WT)
  CPU-like “Read-for-Ownership” cache coherence (RFO)
QuickRelease Implementation
Results
Conclusions / Future work
Notes: Consider removing this slide.

## Slide 8: Synchronization Operations
Traditional synchronization
  Kernel Begin: All stores from CPU and prior kernel completions are visible.
  Kernel End: All stores from a kernel are visible to CPU and future kernels.
  Barrier: All members of a workgroup are at the same PC and all prior stores in program order will be visible.
HSA specification includes Load-Acquire and Store-Release
  Load-Acquire (LdAcq): A load that occurs before all memory operations later in program order (like Kernel Begin).
  Store-Release (StRel): A store that occurs after all prior memory operations in program order (like Kernel End or Barrier).
Notes: Prepare for questions on HSA semantics (CPU reading data).

## Slide 9: Write-Through (WT) Memory System
Clean caches support fast reads
Wavefront coalescing of writes at the CU
Track byte-wise writes
LdAcq -> invalidate entire L1 cache
StRel -> ensure write-through
CPU0
L1
L2
CPU1
L1
L2
CU1
L1
CU0
L1
LLC
Directory / Memory
CPU
GPU

## Slide 10: Read-for-ownership (RfO) memory system
Current CPUs
Single-Writer or Multiple-Readers invariant
Wavefront coalescing of writes at the CU
LdAcq, StRel are simply Ld and St operations
Invalidations, dirty-writeback and data responses
CPU0
L1
L2
CPU1
L1
L2
CU1
L1
CU0
L1
LLC
Directory / Memory
CPU
GPU

## Slide 11: OUTLINE
Motivation
  Current GPUs
  Future GPUs
Memory System Design & Supporting Synchronization
  Write-through with cache flushes (WT)
  CPU-like “Read-for-Ownership” cache coherence (RFO)
QuickRelease
Results
Conclusions / Future work
Notes: Consider removing this slide.

## Slide 12: QuickRelease BASICS
Coherence by “begging for forgiveness” instead of “asking for permission”
Separate read and write paths
Track byte-wise writes to avoid reading for ownership
Coalesce writes across wavefronts
  Supports irregular local writes and local read-after-writes (RAW)
  Reduces traffic of write-throughs
Only invalidate necessary blocks
  Reuse data across synchronization
  Overlap invalidations with writes to memory
  Precise: only synchronization stalls on invalidation acks
Notes: Byte wise writes tracked without read-for-ownership

## Slide 13: QuickRelease: Efficient synchronization & sharing
Use FIFOs and write caches to support store visibility
Lazily invalidate read caches to maintain coherence
CPU0
L1
L2
CPU1
L1
rL2
CU1
rL1
wL2
wL1
CU0
rL1
wL1
wL3
LLC
Directory / Memory
CPU
GPU
S-FIFO
S-FIFO
S-FIFO
S-FIFO

## Slide 14: QuickRelease Example
LD_Acq A (2)
LD X (1)
ST X (1)
ST_Rel A (2)
CU0
CU1
CU0
L1
X: 1
MEM
X: 0
A: 0
CU1
FIFO
X
…

## Slide 15: QuickRelease Example
LD_Acq A (2)
LD X (1)
ST X (1)
ST_Rel A (2)
CU0
CU1
CU0
L1
X: 1
MEM
X: 0
A: 0
CU1
FIFO
X
Rel
…

## Slide 16: QuickRelease Example
LD_Acq A (2)
LD X (1)
ST X (1)
ST_Rel A (2)
CU0
CU1
CU0
L1
X: 1
MEM
X: 1
A: 0
FIFO
X
Rel
CU1
L1
A: 1
X: #
FIFO

## Slide 17: QuickRelease Example
LD_Acq A (2)
LD X (1)
ST X (1)
ST_Rel A (2)
CU0
CU1
CU0
L1
X: 1
MEM
X: 1
A: 0
FIFO
Rel
CU1
…

## Slide 18: QuickRelease Example
LD_Acq A (2)
LD X (1)
ST X (1)
ST_Rel A (2)
CU0
CU1
CU0
L1
A: 2
MEM
X: 1
A: 2
FIFO
A
CU1
L1
A: #
X:#
FIFO

## Slide 19: QuickRelease Example
LD_Acq A (2)
LD X (1)
ST X (1)
ST_Rel A (2)
CU0
CU1
CU0
L1
MEM
X: 1
A: 2
FIFO
CU1
L1
A: 2
X:1
FIFO

## Slide 20: RECAP: QuickRelease vs rfo and wt
Design Goals | WT | RFO | QuickRelease
High bandwidth | YES | NO | YES
Only wait on synchronization | YES | NO | YES
Avoids L1 data responses | YES | NO | YES
Coalesce irregular writes | NO | YES | YES
Precise Cache invalidations | NO | YES | YES
Support RAW | NO | YES | YES

## Slide 21: OUTLINE
Motivation
  Current GPUs
  Future GPUs
Memory System Design & Supporting Synchronization
  Write-through with cache flushes (WT)
  CPU-like “Read-for-Ownership” cache coherence (RfO)
QuickRelease
Results
Conclusions / Future work
Notes: Consider removing this slide.

## Slide 22: Benchmarks
Synchronizing applications
  APSP: converging on All-Pairs Shortest Path (uses LdAcq and StRel)
  Sort: performs a 4-byte radix sort byte by byte (uses LdAcq and StRel)
Rodinia benchmarks
  nn: n-nearest neighbors
  backprop: trains the connection weights on a neural network
  hotspot: performs a transient 2D thermal simulation (5-point stencil)
  lud: matrix decomposition
  kmeans: does k-means clustering
  nw: performs a global optimization for DNA sequence alignment
AMD APP SDK
  nbody: simulation of particle-particle interactions
  matrixmul: multiplies matrices
  reduction: sums the values in an input array
  dct: algorithm for image and video frame compression

## Slide 23: Read after Read REUSE in L1
Chart: Read hit in L1 per read issued
| sort | dct | hotspot | nn | backprop | reduction | bitonic | APSP | lud | kmeans | histogram | matrixmul | bfs | srad | spmv | nw | Mean
RAR reuse | 0.96326 | 0.71702 | 0.59385 | 0.40217 | 0.39727 | 0.37246 | 0.35064 | 0.29715 | 0.24939 | 0.22158 | 0.19659 | 0.093905 | 0.092938 | 0.070746 | 0.06195 | 0.00082812 | 0.31761
Notes: WHY intermediate reuse matters so much
Read after read explain better

## Slide 24: Performance of QuickRelease vs. WT and rfo
Chart: runtime relative to no L1
| sort | dct | hotspot | nn | backprop | reduction | bitonic | APSP | lud | kmeans | histogram | matrixmul | bfs | srad | spmv | nw | Mean
noL1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
WT | 0.97434 | 1.0118 | 0.69411 | 0.78922 | 0.98641 | 0.68245 | 0.96567 | 1.3265 | 1.0479 | 0.99971 | 1.0001 | 0.92533 | 0.92953 | 0.99996 | 0.99994 | 1.0039 | 0.9474
RFO | 0.97761 | 1.0355 | 1.0257 | 1.3381 | 1.0608 | 1.314 | 1.1834 | 0.23137 | 1.1702 | 1.0389 | 1.1281 | 1.6477 | 1.4985 | 1.0043 | 1.0873 | 1.4101 | 1.0656
QR | 0.97786 | 0.93773 | 0.50746 | 0.72947 | 0.99183 | 0.64989 | 0.73922 | 0.77541 | 1.1665 | 1.0008 | 1.0049 | 0.92973 | 0.89477 | 1.0009 | 1.0073 | 1.0367 | 0.8794
Notes: Animate bars in order

## Slide 25: Performance of QuickRelease vs. WT and rfo
Chart: runtime relative to no L1
| sort | dct | hotspot | nn | backprop | reduction | bitonic | APSP | lud | kmeans | histogram | matrixmul | bfs | srad | spmv | nw | Mean
noL1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
WT | 0.97434 | 1.0118 | 0.69411 | 0.78922 | 0.98641 | 0.68245 | 0.96567 | 1.3265 | 1.0479 | 0.99971 | 1.0001 | 0.92533 | 0.92953 | 0.99996 | 0.99994 | 1.0039 | 0.9474
RFO | 0.97761 | 1.0355 | 1.0257 | 1.3381 | 1.0608 | 1.314 | 1.1834 | 0.23137 | 1.1702 | 1.0389 | 1.1281 | 1.6477 | 1.4985 | 1.0043 | 1.0873 | 1.4101 | 1.0656
QR | 0.97786 | 0.93773 | 0.50746 | 0.72947 | 0.99183 | 0.64989 | 0.73922 | 0.77541 | 1.1665 | 1.0008 | 1.0049 | 0.92973 | 0.89477 | 1.0009 | 1.0073 | 1.0367 | 0.8794
Notes: Animate bars in order

## Slide 26: Performance of QuickRelease vs. WT and rfo
Chart: runtime relative to no L1
| sort | dct | hotspot | nn | backprop | reduction | bitonic | APSP | lud | kmeans | histogram | matrixmul | bfs | srad | spmv | nw | Mean
noL1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
WT | 0.97434 | 1.0118 | 0.69411 | 0.78922 | 0.98641 | 0.68245 | 0.96567 | 1.3265 | 1.0479 | 0.99971 | 1.0001 | 0.92533 | 0.92953 | 0.99996 | 0.99994 | 1.0039 | 0.9474
RFO | 0.97761 | 1.0355 | 1.0257 | 1.3381 | 1.0608 | 1.314 | 1.1834 | 0.23137 | 1.1702 | 1.0389 | 1.1281 | 1.6477 | 1.4985 | 1.0043 | 1.0873 | 1.4101 | 1.0656
QR | 0.97786 | 0.93773 | 0.50746 | 0.72947 | 0.99183 | 0.64989 | 0.73922 | 0.77541 | 1.1665 | 1.0008 | 1.0049 | 0.92973 | 0.89477 | 1.0009 | 1.0073 | 1.0367 | 0.8794
Notes: Animate bars in order

## Slide 27: Performance of QuickRelease vs. WT and rfo
Chart: runtime relative to no L1
| sort | dct | hotspot | nn | backprop | reduction | bitonic | APSP | lud | kmeans | histogram | matrixmul | bfs | srad | spmv | nw | Mean
noL1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
WT | 0.97434 | 1.0118 | 0.69411 | 0.78922 | 0.98641 | 0.68245 | 0.96567 | 1.3265 | 1.0479 | 0.99971 | 1.0001 | 0.92533 | 0.92953 | 0.99996 | 0.99994 | 1.0039 | 0.9474
RFO | 0.97761 | 1.0355 | 1.0257 | 1.3381 | 1.0608 | 1.314 | 1.1834 | 0.23137 | 1.1702 | 1.0389 | 1.1281 | 1.6477 | 1.4985 | 1.0043 | 1.0873 | 1.4101 | 1.0656
QR | 0.97786 | 0.93773 | 0.50746 | 0.72947 | 0.99183 | 0.64989 | 0.73922 | 0.77541 | 1.1665 | 1.0008 | 1.0049 | 0.92973 | 0.89477 | 1.0009 | 1.0073 | 1.0367 | 0.8794
Notes: Animate bars in order

## Slide 28: Conclusions
QuickRelease (QR) gets the best of both worlds (RFO and WT)
  High streaming bandwidth
  Efficient fine-grain communication and synchronization
QR achieves 7% average performance improvement compared to WT
For emerging workloads with finer-grain synchronization, 42% performance improvement compared to WT
QuickRelease Costs
  Separate read and write caches
  Synchronization FIFOs
  Probe broadcast to CUs
Notes: MJS – Added “For QuickRelease”.
Overall 7% not bad, furthermore fine-grain

## Slide 29: Questions?

## Slide 30: Disclaimer & Attribution
The information presented in this document is for informational purposes only and may contain technical inaccuracies, omissions and typographical errors.
The information contained herein is subject to change and may be rendered inaccurate for many reasons, including but not limited to product and roadmap changes, component and motherboard version changes, new model and/or product releases, product differences between differing manufacturers, software changes, BIOS flashes, firmware upgrades, or the like. AMD assumes no obligation to update or otherwise correct or revise this information. However, AMD reserves the right to revise this information and to make changes from time to time to the content hereof without obligation of AMD to notify any person of such revisions or changes.
AMD MAKES NO REPRESENTATIONS OR WARRANTIES WITH RESPECT TO THE CONTENTS HEREOF AND ASSUMES NO RESPONSIBILITY FOR ANY INACCURACIES, ERRORS OR OMISSIONS THAT MAY APPEAR IN THIS INFORMATION.
AMD SPECIFICALLY DISCLAIMS ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE. IN NO EVENT WILL AMD BE LIABLE TO ANY PERSON FOR ANY DIRECT, INDIRECT, SPECIAL OR OTHER CONSEQUENTIAL DAMAGES ARISING FROM THE USE OF ANY INFORMATION CONTAINED HEREIN, EVEN IF AMD IS EXPRESSLY ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.
ATTRIBUTION
© 2014 Advanced Micro Devices, Inc. All rights reserved. AMD, the AMD Arrow logo and combinations thereof are trademarks of Advanced Micro Devices, Inc. in the United States and/or other jurisdictions. SPEC is a registered trademark of the Standard Performance Evaluation Corporation (SPEC). Other names are for informational purposes only and may be trademarks of their respective owners.

## Slide 31: Scalability of QuickRelease vs. rfo
QuickReleae outperforms RFO when problem sizes are beyond cache capacity
Chart: Run-time of reduction
| 16384 | 262144
noL1 | 15808 | 307792
WT | 9576 | 214272
RfO | 9820 | 413864
QR | 9904 | 202360
Chart: Run-time of nn
| 4 | 8 | 32
noL1 | 45008 | 85020 | 327200
WT | 27008 | 49688 | 261792
RfO | 30804 | 64628 | 440308
QR | 27660 | 50288 | 234648

## Slide 32: QuickRelease Example
 LD_Acq A (2)
 LD X (1)
 ST X (1)
 ST_Rel A (2)
CU0
CU1
CU0
L1
X: 1
MEM
X: 0
A: 0
CU1
FIFO
X
Rel


…
CU0
L1
A: 2
MEM
X: 1
A: 2
FIFO
A

CU1
L1
A: 2
X:1
FIFO

CU0
L1
X: 1
MEM
X: 1
A: 0
FIFO
X
Rel


CU1
…
CU0
L1
MEM
X: 1
A: 2
FIFO
CU1
L1
A: 2
X:1
FIFO



Time

## Slide 33: WT Example
 LD_Acq A (2)
 LD X (1)
 ST X (1)
 ST_Rel A (2)
CU0
CU1
CU0
L1
X: 1
MEM
X: 0
A: 0

CU1
L1
Y: 3


CU0
L1
X: 1
MEM
X: 1
A: 0
CU1
L1
Y: 3


CU0
L1
MEM
X: 1
A: 0
CU1
L1
Y: 3

CU0
L1
A: 2
MEM
X: 1
A: 2
CU1
L1
Y: 3


CU0
L1
A: 2
MEM
X: 1
A: 2
CU1
L1


CU0
L1
A: 2
MEM
X: 1
A: 2
CU1
L1
A: 2
X: 1


Time

## Slide 34: RFO Example
 LD_Acq A (2)
 LD X (1)
 ST X (1)
 ST_Rel A (2)
CU0
CU1
CU0
L1
X: 1
MEM
X: 0
A: 0

CU1
L1
Y: 3

CU0
L1
A: 2
MEM
X: 1
A: 0
CU1
L1
Y: 3
Time
CU0
L1
A: 2
MEM
X: 1
A: 2
CU1
L1



CU0
L1
X: 1
MEM
X: 1
A: 2
CU1
L1




## Slide 35: Reduction of write-throughs
Chart: Relative Write-throughs
| sort | dct | hotspot | nn | backprop | reduction | bitonic | APSP | lud | kmeans | histogram | matrixmul | bfs | srad | spmv | nw | Mean
noL1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
WT | 0.99953 | 0.95403 | 0.91998 | 1.0124 | 0.98898 | 0.85092 | 0.99843 | 2.9002 | 0.99123 | 0.97906 | 0.91639 | 0.96377 | 0.97829 | 0.93395 | 1.0003 | 1 | 1.0335
QR | 0.92738 | 0.79878 | 0.43764 | 1.0052 | 0.83743 | 0.40604 | 0.58912 | 0.90852 | 0.811 | 0.85099 | 0.85439 | 0.99716 | 0.90094 | 0.9287 | 0.80926 | 0.99998 | 0.79126

## Slide 36: Probes versus data
Probes create a lot of traffic, but QuickRelease reduces data messages
Chart: Bytes received QR/bytes recved WT
| sort | dct | hotspot | nn | backprop | reduction | bitonic | APSP | lud | kmeans | histogram | matrixmul | bfs | srad | spmv | nw | Mean
L1_Data | 0.59594 | 0.88243 | 0.90361 | 0.7602 | 1.0221 | 0.93236 | 0.99536 | 0.37873 | 0.95415 | 0.99937 | 0.99777 | 0.99955 | 0.97044 | 0.97801 | 0.99915 | 0.9983 | 0.87442
L1_Probes | 0.31723 | 1.0243 | 0.40991 | 0.31459 | 0.53617 | 0.0057894 | 0.90626 | 0.010801 | 0.36384 | 0.034135 | 0.031651 | 0.32772 | 0.29273 | 1.698 | 0.34556 | 1.3001 | 0.22271
More writes than reads
CPU probes

## Slide 37: Why GPUs should not have write-back caches
Chart: Fraction of loads hitting written data
| sort | dct | hotspot | nn | backprop | reduction | bitonic | APSP | lud | kmeans | histogram | matrixmul | bfs | srad | spmv | nw | Mean
RAW reuse | 3.5031e-05 | 0 | 0 | 0 | 0.0044336 | 0 | 0.0013053 | 0.0069174 | 0.0097053 | 0 | 0.005988 | 0.0081397 | 0.0044074 | 0.0029664 | 0 | 0.00068359 | 0.0027864