## Slide 1: FreshCache: Statically and Dynamically Exploiting Dataless Ways
Arkaprava Basu, Derek R. Hower, Mark D. Hill, Mike M. Swift

## Slide 2: Last Level Caches: Area and Energy Hungry
Intel Ivy Bridge die picture
Notes: Large portion of on-chip die area is often devoted to LLC sometimesup to 50%

## Slide 3: Last Level Caches: Area and Energy Hungry
LLC contributes up to 37% of on-chip power [Sen et al., 2013, UW-TR 1791]
Intel Ivy Bridge die picture
Notes: Due to static power and since large number of transistors devoted to LLC they can contribute substantially to chip power.

## Slide 4: Inefficiencies in LLC
Inclusive LLC wastes energy and area
  Transistors devoted to hold stale data
Notes: However there are many inefficiencies in LLC, especially in commercially popular inclusive LLC where every block in the private caches of cores has a copy in the LLC.
For example in this case the block A is cached with exclusive permission at the C1’s private cache and a copy of which is present in the LLC. The C1 can update the content of the block without notifying the LLC.
Later if a core C2 requests the same cache line the tag and coherence meta data of the block present in the LLC is used to identify the owner of the block but the data portion of the block in the LLC is not usable. We cal this block with satle data. And transistors devoted to it is waste.
Talk about non modification case

## Slide 5: Inefficiencies in LLC
Inclusive LLC wastes energy and area
  Transistors devoted to hold stale data
LLC + Directory
Private Caches (L1/L2)
C1
C2
A :x
A :x
TAG
DATA
Block A is cached with exclusive permission in C1’s private cache
A :y
Notes: However there are many inefficiencies in LLC, especially in commercially popular inclusive LLC where every block in the private caches of cores has a copy in the LLC.
For example in this case the block A is cached with exclusive permission at the C1’s private cache and a copy of which is present in the LLC. The C1 can update the content of the block without notifying the LLC.
Later if a core C2 requests the same cache line the tag and coherence meta data of the block present in the LLC is used to identify the owner of the block but the data portion of the block in the LLC is not usable. We cal this block with satle data. And transistors devoted to it is waste.
Talk about non modification case

## Slide 6: Inefficiencies in LLC
Inclusive LLC wastes energy and area
  Transistors devoted to hold stale data
Amount of stale data varies across workloads
Fraction of stale data in LLC blocks
Chart: 
| blackscholes | canneal | facesim | fluidanimate | freqmine | streamcluster | swaptions | x264 | graph500 | memcached | SpecJBB | Mean
 | 0.23858 | 0.16955 | 0.27431 | 0.22377 | 0.19301 | 0.25538 | 0.70701 | 0.18376 | 0.1076 | 0.1453 | 0.17339 | 0.23679
 | 0.23858 | 0.16955 | 0.27431 | 0.22377 | 0.19301 | 0.25538 | 0.70701 | 0.18376 | 0.1076 | 0.1453 | 0.17339 | 0.23679
0.7
Private Cache: LLC ratio ~ 1:4
Notes: What is important is that the the amount of cache blocks with stale data varies across the workloads

## Slide 7: Idea: FreshCache
Static:
  Omit data portion of a fixed number of ways
  Reduce area and energy overhead
Dynamic :
  Disable data ways at runtime
  Reduce more energy for when possible

## Slide 8: Roadmap
Motivation and key idea
FreshCache: Static + Dynamic Dataless Ways
Design and Mechanisms
Evaluation
Summary

## Slide 9: Static Dataless Ways (SDWs)
TAG + Metadata
Data
Set
Way
Set-associative LLC

## Slide 10: Static Dataless Ways (SDWs)
Set-associative LLC
Number of dataless ways fixed at design time
Static Dataless Way
✔
Saves both area and static power*
✗
Cannot adapt to workloads
* If blocks with stale data kept in SDWs

## Slide 11: Dynamic Dataless Ways (DDWs)
Set-associative LLC
Number of dataless ways adjusted at runtime
Data ways Turned off
Workload A
Dynamic Dataless Ways

## Slide 12: Dynamic Dataless Ways (DDWs)
Set-associative LLC
Number of dataless ways adjusted at runtime
Workload B
Cache utilization is less for workload B
Notes: Workloads B is less cache sensitive than workload A.

## Slide 13: Dynamic Dataless Ways (DDWs)
Set-associative LLC
Number of dataless ways adjusted at runtime
Data ways Turned off
Workload B
✔
Opportunistically save more energy
✗
No area savings

## Slide 14: FreshCache Goals: Best of Both Worlds
Static: save area and energy
  Omitting transistors at design time
Dynamic: save more energy
  Turning off transistor when possible
How to tradeoff performance?
  Bounded by Maximum Performance Degradation
    e.g., MPD = 1% or 3%
  Minimize energy subject to MPD

## Slide 15: FreshCache: Static + Dynamic Dataless Ways
Workload A/B
Static Dataless Ways
Dynamic Dataless Ways

## Slide 16: FreshCache: Challenges
Put blocks with stale data in dataless ways
Determine number of DDWs at runtime
1
2

## Slide 17: Roadmap
Motivation
FreshCache: Static + Dynamic Dataless Ways
Mechanisms
  LLC Controller  Manage Dataless ways
  DDW Controller  Determine number of DDWs
Evaluation
Summary
1
2

## Slide 18: Dataless-Way-Aware LLC Controller
Coherence state decides if cache block put in dataless way
From Memory/Other Socket
Keep blocks with stale data in dataless ways
1
Exclusive state
SDW or DDW

## Slide 19: Dataless-Way-Aware LLC Controller
Coherence state decides if cache block put in dataless way
From Memory/Other Socket
Keep blocks with stale data in dataless ways
1
Shared state
SDW or DDW

## Slide 20: Dataless-Way-Aware LLC Controller
Writeback to dataless way may move block to conventional way
Intra-set block movement
Keep blocks with stale data in dataless ways
1
Writeback from Private $

## Slide 21: DDW Controller
Determines number of DDWs at runtime
DDW Cont.
LLC miss Estimator
Avg. Mem. Latency
Hit Counters
Maximum Performance Degradation (MPD)
Energy savings
Est. LLC miss
Aggregator
Aux. Tag Array
2
Software specifies performance vs. energy savings tradeoff
MPD value specified in a register
Energy savings subjected to MPD
Qureshi’06
0.3% overhead

## Slide 22: DDW Controller
Determines number of DDWs at runtime
DDW Cont.
LLC miss Estimator
Avg. Mem. Latency
Hit Counters
Maximum Performance Degradation (MPD)
Energy savings
Est. LLC miss
Aggregator
Aux. Tag Array
2
Qureshi’07

## Slide 23: Roadmap
Motivation
FreshCache: Static + Dynamic Dataless Ways
Mechanisms
Evaluation
Summary

## Slide 24: Methodology
gem5 full system simulation
8 in-order cores, 3-level cache hierarchy
Parsec and commercial workloads
CACTI 6.5 to evaluate area and energy savings
Evaluation:
  Efficacy of FreshCache in saving energy
  Area savings due to FreshCache

## Slide 25: Energy Savings: MPD=1%
Relative Energy (LLC + DRAM access) Savings
28%
2 SDWs (out 16 ways) + variable number of DDWs
Percentage (%)
Avg. 28% energy savings with worst case perf. Degradation < 1%

## Slide 26: Energy Savings: MPD= 3%
Relative Energy (LLC + DRAM access) Savings
28%
41%
2 SDWs (out 16 ways) + variable number of DDWs
MPD = 1%
Percentage (%)
Avg. 41% energy savings with worst case perf. Degradation < 3%

## Slide 27: Area Savings
Relative Energy (LLC + DRAM access) Savings
28%
41%
2 SDWs (out 16 ways) + variable number of DDWs
MPD = 1%
Percentage (%)
8.23% of LLC area saved

## Slide 28: Summary
LLC can be energy and area hungry
Inclusive LLCs holds substantial stale data
FreshCache:
  Static Dataless Ways to save area and power
  Dynamic Dataless Ways to save further power
28% Energy and 8.23% LLC area savings
  Worst case performance degradation <1%