## Slide 1: Rerun: Exploiting Episodes for Lightweight Memory Race Recording
Derek R. Hower and Mark D. Hill
  Computer systems complex – more so with multicore
  What technologies can help?
Notes: Thank you. In this talk, I will address a fundamental problem with modern computer systems, namely that they are incredibly complex to design and manage. The advent of the multicore era is only making that problem worse due to complexities that arise in multithreaded programming. To overcome this, I believe we should ask ourselves the question: what technologies can help? SOFTWARE IS COMPLEX

## Slide 2: Executive Summary
State of the Art
  Deterministic replay can help
  Uniprocessor replay can be done in hypervisor
  Multiprocessor replay must record memory races
  Existing HW race recorders
    Too much state (e.g., 24KB ) or don’t scale to many processors
We Propose: Rerun
  Record Memory Races?
  Record Lack of Memory Races – An Episode
  Best log size (like FDR-2): 4 bytes/1000 instructions
  Best state (like Strata-snoop) : 166 bytes/core
NO
Notes: Big Picture: Industry feedback said hardware state needed reduced…we did so without sacrificing log performance

## Slide 3: Outline
Motivation
  Deterministic Replay
  Memory Race Recording
Episodic Recording
Rerun Implementation
Evaluation
Conclusion

## Slide 4: Deterministic Replay (1/2)
Deterministic Replay
  Faithfully replay an execution such that all instructions appear to complete in the same order and produce the same result
Valuable
  Debugging [LeBlanc, et al. - COMP ’87]
    e.g., time travel debugging, rare bug replication
  Fault tolerance [Bressoud, et al. - SIGOPS ‘95]
    e.g., hot backup virtual machines
  Security [Dunlap et al. – OSDI ‘02]
    e.g., attack analysis
  Tracing [Xu et al. – WDDD ‘07]
    e.g., unobtrusive replay tracing

## Slide 5: Deterministic Replay (2/2)
Implementation: Must Record Non-Deterministic Events
  Uniprocessors: I/O, time, interrupts, DMA, etc.
  Okay to do in software or hypervisor
Multiprocessor Adds: Memory Races
  Nondeterministic
  Almost any memory reference could race  Record w/ HW?
X = 0
X = 5
if (X > 0)
Launch Mark
X = 0
X = 5
if (X > 0)
Launch Mark
T0
T1
T0
T1
X = 0
X = 5
if (X > 0)
Launch Mark
T0
T1

## Slide 6: Memory Race Recording
Problem Statement
  Log information sufficient to replay all memory races in the same order as originally executed
Want
  Small log – record longer for same state
  Small hardware – reduce cost, especially when not used
  Unobtrusive – should not alter execution
State of the Art
  Wisconsin Flight Data Recorder 1 & 2 [ISCA’03 & ASPLOS’06]
  4 bytes/1000 instructions log but 24 KB/processor
  UCSD Strata [ASPLOS’06]
  0.2 KB/processor, but log size grows rapidly with more cores
Notes: FDR remembers individual races and then performs an explicit analysis to determine which ones are implied through transitivity and can be ignored
Strata reduces the hardware requirement of FDR by logging global sections of race-free code. However, as our results later will show, because they store a global log entry, the log size may grow quickly as the number of cores increase.

## Slide 7: Outline
Motivation
Episodic Recording
  Record lack of races
Rerun Implementation
Evaluation
Conclusion

## Slide 8: Episodic Recording
Most code executes without races
  Use race-free regions as unit of ordering
Episodes: independent execution regions
  Defined per thread
  Identified passively  does not affect execution
  Encompass every instruction
T0
T1
LD A
ST B
ST C
LD F
ST E
LD B
ST X
LD R
ST T
LD X
T2
ST V
ST Z
LD W
LD J
ST C
LD Q
LD J
ST Q
ST E
ST C
LD Z
LD V
ST X
Notes: No speculation/rollback support needed.

## Slide 9: Capturing Causality
23
Via scalar Lamport Clocks [Lamport ‘78]
  Assigns timestamps to events
  Timestamp order implies causality
Replay in timestamp order
  Episodes with same timestamp can be replayed in parallel
43
22
60
61
44
62
23
44
45
T0
T1
T2
Notes: Event with lower timestamp occurs causally before an event with a higher timestamp
-References don’t need to be replayed in the same order…just races! Replaying in timestamp order preserves race ordering!

## Slide 10: Episode Benefits
Multiple races can be captured by a single episode
  Reduces amount of information to be logged
Episodes are created passively
  No speculation, no rollback
Episodes can end early
  Eases implementation
Episode information is thread-local
  Promotes scalability, avoids synchronization overheads

## Slide 11: Outline
Motivation
Episodic Recording
Rerun Implementation
  Added hardware
  Extensions & Limitations
Evaluation
Conclusion

## Slide 12: Hardware
Rerun requirements:
  Detect races  track r/w sets
  Mark episode boundaries
  Maintain logical time
Data
Tags
Directory
Coherence Controller
Coherence Controller
L1 I
L1 D
Pipeline
L2 0
L2 1
L2 14
L2 15
Core 15
Interconnect
DRAM
DRAM
…
Core 14
Core 1
Core 0
…
Rerun Core State
Base System
Write Filter (WF)
Read Filter (RF)
Timestamp (TS)
References (REFS)
Rerun L2/Memory State
Memory Timestamp(MTS)
32 bytes
128 bytes
2 bytes
4 bytes
4 bytes
Total State: 166 bytes/core
Notes: Can use filters to detect when races occur…when two accesses are to the same address and at least one is a write
Directory protocol!!

## Slide 13: Putting it All Together
Thread 0
Thread 1
A
R
T
REFS: 16
TS: 42
…
R: {}
W: {}
REFS: 0
TS: 6
R: {}
W: {}
REFS: 0
TS: 43
ST F
LD A
ST B
ST F
REFS: 97
TS: 5
…
LD R
ST T
LD F
ST B
R: {}
W: {F}
REFS: 1
TS: 43
R: {A}
W: {F}
REFS: 2
TS: 43
R: {R}
W: {}
REFS: 1
TS: 6
R: {A}
W: {F,B}
REFS: 3
TS: 43
R: {R}
W: {T}
REFS: 2
TS: 6
R: {A}
W: {F,B}
REFS: 4
TS: 43
RACE!
F
TS: 43
R: {R,F}
W: {T}
REFS: 3
TS: 44
REFS: 4
TS: 43
R: {}
W: {}
REFS: 0
TS: 44
B
TS: 44
R: {R,F}
W: {T,B}
REFS: 4
TS: 45

## Slide 14: Implementation Recap
Bloom filters to track read/write set
  False positives O.K.
Reference counter to track episode size
Scalar timestamps at cores, shared memory
Piggyback timestamp data on coherence responses
Log episode duration and timestamp

## Slide 15: Extensions & Limitations
Extensions to base system:
  SMT
  TSO, x86 memory consistency models
  Out of Order cores
  Bus-based or point-to-point snooping interconnect
Limitations:
  Write-through private cache reduces log efficiency
  Mostly sequential replay
  Relaxed/weak memory consistency models
Notes: Logging efficiency of Rerun is tied into the write-back design of a private L1 cache. More work is needed to extend Rerun into systems with a write through private cache.

## Slide 16: Outline
Motivation
Episodic Recording
Rerun Implementation
Evaluation
  Methodology
  Episode characteristics
  Performance
Conclusion

## Slide 17: Methodology
Full system simulation using Wisconsin GEMS
  Enterprise SPARC server running Solaris
Evaluated on four commercial workloads
  2 static web servers (Apache and Zeus)
  OLTP-like database (DB2)
  Java middleware (SpecJBB2000)
Base system:
  16 in-order core CMP
  32K 4-way write-back L1, 8M 8-way shared L2
  MESI directory protocol, sequential consistency
Notes: Workloads are a likely target for replay based on the usages described before.

## Slide 18: Episode Characteristics
Use perfect (no false positive) Bloom filters, unlimited resources
~64K
70
113
2 byte REFS counter
Episode Length CDF
# dynamic memory refs
Write Set Size
Read Set Size
# blocks
# blocks
Filter Sizes: 32 & 128 bytes
Notes: Episodes are long enough to compress the log, and small filters are sufficient to allow for long episodes

## Slide 19: Log Size
~ 4 bytes/1000 instructions uncompressed
Chart: Bytes/Kilo-instr
| Apache | JBB | OLTP | Zeus | Avg
Series 1 | 4.958 | 2.9036 | 3.2692 | 4.5335 | 3.7287

## Slide 20: Comparison – Log Size
Chart: Bytes/Kilo-instr
| 2p | 4p | 8p | 16p
Rerun | 1.896 | 3.576 | 4.12 | 3.728
FDR-2 | 1.7177 | 3.47 | 4.58 | 2.8
Strata | 6.96 | 25.24 | 58 | 108.48
58
108
Good Scalability

## Slide 21: Comparison – Hardware State
Chart: # cores
| 4.0 | 8.0 | 16.0 | 24.0 | 32.0 | 48.0 | 64.0 | 72.0 | 96.0 | 128.0 | 144.0 | 172.0 | 200.0 | 256.0
FDR-2 | 96.156 | 192.5 | 386 | 580.5 | 776 | 1170 | 1568 | 1768 | 2376 | 3200 | 3618 | 4359 | 5112 | 6656
Strata | 0.77 | 1.53 | 3.06 | 4.59 | 6.125 | 9.1875 | 12.25 | 13.78 | 18.375 | 24.5 | 27.56 | 32.92 | 38.28 | 49
Rerun | 0.66 | 1.33 | 2.66 | 3.98 | 5.31 | 7.97 | 10.63 | 11.95 | 15.9375 | 21.25 | 23.91 | 28.55 | 33.2 | 42.5
Good Scalability and Small Hardware State

## Slide 22: Conclusion
State of the Art
  Deterministic replay can help
  Uniprocessor replay can be done in hypervisor
  Multiprocessor replay must record memory races
  Existing HW race recorders
    Too much state (e.g., 24KB ) & don’t scale to many processors
We Propose: Rerun – Replay Episodes
  Record Lack of Memory Races
  Best log size (like FDR-2): 4 bytes/1000 instructions
  Best state (like Strata-snoop) : 166 bytes/core

## Slide 23: Questions?

## Slide 24: Delorean vs. Rerun
 | Delorean | Rerun
Ordering | Sequential | Distributed
Extensibility | Low | High
Log Size | Very Small | Small
Replay | Mostly Parallel | Mostly Sequential

## Slide 25: From 10,000 Feet
Rerun is a lightweight memory race recorder
  One part of full deterministic replay system
Rerun in HW, rest in HW or SW
Pipeline
Cache Controller
Rerun
Hypervisor
Private Log
Input Logger
Operating System
User Application
HW
SW
Notes: Talk briefly about uses of deterministic replay.

## Slide 26: Adapting to TSO
Violation in TSO…Given block B:
  B in write buffer, and
  Bypassed load of B occurred, and
  Remote request made for B before it leaves the write buffer
On detection, log value of load
  Or, log timestamp corresponding to correct value
Believe this works for x86 model as well

## Slide 27: Detecting SC Violations - Example
1
2
1
2
st A,1
Thread I
Thread J
ld B
st B,1
ld A
Recording
A=B=0
1
2
1
2
st A,1
Thread I
Thread J
ld B
st B,1
ld A
Replay
Value Used
A=0
ld A
ld B
st A,1
st B,1
A=0
B=0
st A,1
st B,1
I
WrBuf
Memory System
J
WrBuf
A=0
B=0
WAR
Omitted
Value
Logged
A=0
B=0
A=1
B=1
J Starts to
Monitor A
I Starts to
Monitor B
A Changed!
I Stops
Monitoring B
*animation from Min Xu’s thesis defense

## Slide 28: Flight Data Recorder
Full system replay solution
Logs all asynchronous events
  e.g. DMA, interrupts, I/O
Logs individual memory races
  Manages log growth through transitive reduction
    i.e. races implied through program order + prior logged race
  Requires per-block last access memory
  State for race recording: ~24KByte
  Race log growth rate: ~1byte/kiloinst compressed

## Slide 29: Strata
Creates global log on race detection
  Breaks global execution into “stratums”
  A stratum between every inter-thread dependence
Most natural on bus/broadcast
Logs grow proportional to # of threads

## Slide 30: Bloom Filters
Three design dimensions
  Hash function
  Array size
  # hashes

## Slide 31: Deterministic Replay (2/2)
Implementation: Must Record Non-Deterministic Events
  Uniprocessors: I/O, time, interrupts, DMA, etc.
  Okay to do in software or hypervisor
Multiprocessor Adds: Memory Races
  (1) from different threads, (2) same address,
  (3) at least one write, & (4) execution order not determined
  Almost any memory reference could race  Record w/ HW?

## Slide 32: Putting it All Together
2: LD T
1: ST F
2: LD A
3: ST B
4: ST F
R: {A} W: {F}
REFS: 2
Timestamp: 43
R: {A} W: {B, F}
REFS: 3
Timestamp: 43
R: {..} W: {..}
REFS: 16
Timestamp: 42
R:{A} W:{B, F}
REFS: 4
Timestamp: 43
. . .
. . .
R: {..} W: {..}
REFS: 97
Timestamp: 5
. . .
R:  W: 
REFS: 0
Timestamp: 44
T1
T0
T1
C := 34
r3 := 28
r4 := X
Y := 120
r3 := X
r5 := 14
Z := 35
Q := 78
Y := 54
G := 98
r7 := D
r9 := E
r6 := E
D := r7
S := r4
C := r3
L := r10
R11 := L
Z :=
F := 1
r1 := A
B := 23
F := 0
r3 := R
r4 := T
r1 := F
r2 := B
A := 7
Read F
R: Ø W: Ø
REFS: 0
Timestamp: 43
R: Ø W: {F}
REFS: 1
Timestamp: 43
DATA + TS 43
R: {A} W: {B, F}
REFS: 4
Timestamp: 43
R: Ø W: Ø
REFS: 0
Timestamp: 6
Read B
R: {R}W: Ø
REFS: 1
Timestamp: 6
R: {R, T}W: Ø
REFS: 2
Timestamp: 6
DATA + TS 44
3: LD F
4: LD B
1: LD R
R: {R, T, F}W: Ø
REFS: 3
Timestamp: 44
R: {R, T, F, B} W: Ø
REFS: 4
Timestamp: 45
E1
E2
T0
REFS, Timestamp  Log

## Slide 33: Logging
Must remember:
  Episode boundaries
  Causality information
Log:
  <Episode length, Timestamp>